## Slide 1: 2.4 Example 2 – prepared in March 2018 Comparison between SHAKE and VERSAT-1D at low-moderate level of earthquake shaking: 1D soil column - MODEL
Dynamic effective stress analysis using the finite element approach by Dr. G. Wu
Lecture for CIVL 581 at University of BC by Dr. Guoxi Wu of BC Hydro / Wutec Geot.
  Wutec Geotechnical International
2. Non-Linear

## Slide 2: 2.4 Example 2: Comparison between SHAKE and VERSAT-1D at low-moderate level of earthquake shaking: 7 input crustal ground motions
Dynamic effective stress analysis using the finite element approach by Dr. G. Wu
Lecture for CIVL 581 at University of BC by Dr. Guoxi Wu of BC Hydro / Wutec Geot.
  Wutec Geotechnical International
2. Non-Linear
Table 2.1 Meta Data of the Seven Crustal Earthquake Records

## Slide 3: 2.4 Example 2: Comparison between SHAKE and VERSAT-1D at low-moderate level of earthquake shaking: soil profiles and parameters
Dynamic effective stress analysis using the finite element approach by Dr. G. Wu
Lecture for CIVL 581 at University of BC by Dr. Guoxi Wu of BC Hydro / Wutec Geot.
  Wutec Geotechnical International
2. Non-Linear
No. | Soil Layer Description | Unit Weight (kN/m3) | Shear Wave Velocity, Vs (m/s)
1a | Wet Loose to Compact Sand and Gravel (above water level) | 19.5 (a.wt) | 160
1b | Saturated Loose to Compact Sand and Gravel (below water level) | 21.2 (b. wt) | 300
3 | Compact Gravel to Gravel | 21.2 | 400
4 | Very Stiff to Hard Clay and Silt | 20.4 | 360
5 | Very Dense/Hard Silt and Sand | 21.7 (“elastic base” input) | 450
Table 2.2 Soil Unit Weights and Shear Wave Velocities for SHAKE and VERSAT-1D
Layer | VERSAT-1D Soil Zone # | Soil Layer Description | Gmax (kPa) | KG | c (kPa) | f (°) | Rf
1a | M1 | Wet Loose to Compact Sand and Gravel (a.wt) | 50887 | 502 | 0 | 3 | 1500
1b | M2 | Saturated Layer 1a (b.wt) | 194495 | 1920 | 0 | 35 | 1500
3 | M3 | Compact Gravel to Gravel | 345770 | 3413 | 0 | 35 | 1500
4 | M4 | Very Stiff to Hard Clay and Silt | 269505 | 2660 | 30 | 25 | 750
Elastic base |  | Very Dense/Hard Silt and Sand | Elastic base, Vs = 450 m/s |  |  |  | 
Table 2.3 Soil Stiffness and Strength Parameters for VERSAT-1D (viscous damping 0.5% for mass & stiffness)

## Slide 4: 2.4 Example 2: Comparison between SHAKE and VERSAT-1D at low-moderate level of earthquake shaking: G/Gmax, and damping curves used in SHAKE analyses
Dynamic effective stress analysis using the finite element approach by Dr. G. Wu
Lecture for CIVL 581 at University of BC by Dr. Guoxi Wu of BC Hydro / Wutec Geot.
  Wutec Geotechnical International
2. Non-Linear

## Slide 5: 2.4 Example 2 Comparison between SHAKE and VERSAT-1D: RESULTS - at low-moderate level of earthquake shaking, SHAKE equivalent linear approximation is able to produce very good representation of true soil nonlinear hysteresis behavior
Dynamic effective stress analysis using the finite element approach by Dr. G. Wu
Lecture for CIVL 581 at University of BC by Dr. Guoxi Wu of BC Hydro / Wutec Geot.
  Wutec Geotechnical International
2. Non-Linear

## Slide 6
Dynamic effective stress analysis using the finite element approach by Dr. G. Wu
Lecture for CIVL 581 at University of BC by Dr. Guoxi Wu of BC Hydro / Wutec Geot.
  Wutec Geotechnical International
2. Non-Linear
2.4 Example 2 Comparison between SHAKE and VERSAT-1D: RESULTS - at low-moderate level of earthquake shaking, SHAKE equivalent linear approximation is able to produce very good representation of true soil nonlinear hysteresis behavior