## Slide 1
Step-by-step Procedures FOR:
making the finite element model of the Upper San Fernando Dam
Step 0: Sketch on paper for five soil units

## Slide 2
Make finite elements for 3 areas & SORT:
(1). Start VERSAT-2D Processor by “Accept” terms:
(2). Change view option: VIEW => Draw Marker for Node/Elem => Show Marker Only
(3). under SETTING, load “USF_m_1.log” & under File, load data “USF_1_view_only.sta”
Note: The colored soil units (in previous slide) can be shown by doing the following:
VIEW Model View Options => Show x, y axis; Show Material color
download versat-2d_2024.03MINI_ak-2.4M (run password=“gwu”)

## Slide 3
1. Make finite elements for 3 areas & SORT:
(4). Under File, load model data “USF_1_nodes.sta”
(5). Make Area 1: 100 x 20 by:
(a).TOOLS => Draw finite element grid => enter: 100, 20, 0 => OK
(b) Snap sequentially nodes:
Node1, N14, N15 and Node2 to create the grids below

## Slide 4
1. Make finite elements for 3 areas & SORT:
(6). Make Area 2: 43 x 12 by:
TOOLS => Draw finite element grid => enter: 43, 12, 0 ; OK
Snap sequentially nodes:
N3, N13, N12 and N4 to create the grids below

## Slide 5
1. Make finite elements for 3 areas & SORT
(7). Make Area 3: 23 x 7 by: [under SETTING, load “USF_upper_dam.log” for a larger view]
TOOLS => Draw finite element grid => enter: 23, 7, 0; OK
Snap sequentially nodes
N4, N9, N6 and N5 to create the grids below
(8). sort the Mesh under MODIFY => Clear duplicate nodes => Sort nodes (v)/element(h)
(9). Under File =>SAVE Model Data as “USF_2.sta”; so it can be reloaded if needed.

## Slide 6
2. Make zone boundaries forming the Clay Core & SORT!
(1). under SETTING, load “USF_upper_dam.log”
(2). under TOOLS => draw a line.. ; snap nodes N7 and N11 to create a line;
(3). again, draw a line from nodes N7 to N8;
(4). again, draw a line from nodes N10 to N11;
(5). sort the Mesh under MODIFY => Clear duplicate nodes => Sort nodes (v)/element(h);
Total 2835 nodes, 2704 elements ;
mesh creation completed!
(6). under File, SAVE model data to “USF_3_mesh.sta” for future use (if required).

## Slide 7
3. Assign soil unit no. for all zones; Define soil parameters, Adjust D/S layer thickness, Set RUNs (layers, water tables, etc.), boundary, water loads (in RUN4)
(1). under TOOLS => Assign soil zones; snap nodes N7, N11, N10, N8; type 3 (Clay Core) for the input box; refresh view to see blue zone (shown below)
(2). do the same for all other soil zones
(3). under File, SAVE model data to “USF_4_temp.sta” for recovery, if required.

## Slide 8
3. Assign soil unit no. for all zones; Define soil parameters, Adjust D/S layer thickness, Set RUNs (layers, water tables, etc.), boundary, water loads (in RUN4)
(4). do the same for all other soil zones (note: Use No. 6 for hydraulic fill above water)
under SETTING => load “USF_Model.log” and refresh view (with Show Material color on)

## Slide 9
3. Assign soil unit no. for all zones; Define soil parameters, Adjust D/S layer thickness, Set RUNs (layers, water tables, etc.), boundary, water loads (in RUN4)
(5). RUN1: under DEFINE => setup static analysis => Add a layer: 1000 elements; repeat
for 500, 509; APPLY and EXIT SETUP; refresh view with “Show layers by color” ON

## Slide 10
3. Assign soil unit no. for all zones; Define soil parameters, Adjust D/S layer thickness, Set RUNs (layers, water tables, etc.), boundary, water loads (in RUN4)(5).
(6) Under DEFINE => Input material parameters, as per table below [APPLY ALL]
(use Kg/3 and Kb/3 for static analysis; use the same parameters for No. 2 and No. 6)
(7). under DEFINE => setup static analysis => click “NEW RUN” to setup RUN 2, 3, and 4
(see USF_4-FINAL.sta for more details on sequence of static analysis, RUN 1, 2, 3, &4)
(8). re-load setting file: “USF_m_1.log”
Under TOOLS => Assign boundary …; snap two nodes at the base to assign “fixed”;
also do two side boundaries (“free Y”); refresh view with “Show boundary..” ON

## Slide 11
3. Assign soil unit no. for all zones; Define soil parameters, Adjust D/S layer thickness,
Set RUNs (layers, water tables, etc.), boundary, water loads (in RUN4)
(9). In RUN4, apply water loads on the model surface under the reservoir
note: pressure values = 9.81 x water head from reservoir to the surface.
(a). under TOOLS=> Apply distributed load, snaps nodes N2, N3, and enter two pressure
values of “156.0” that normal to the surface;
(b). also for N3, N4 with “156.0” and “39.1” as values;
(c). also for N4, N1078 with “39.1” and “0” as values.
Refresh view with “show load vectors” ON
(10) under File, SAVE model data to “USF_4_FINAL.sta”; ready for RUN

## Slide 12
4. Final Check & RUN
(1). Check model RUN3:
re-load setting file: “USF_Model.log” ;
refresh view with “Show layers by color” “Show boundary..”, “Show load vectors”
and “Show water leel” “Show x, y axis” ON
Note: RUN2 only applies the water table (blue line in the figure below) in 4 increments.

## Slide 13
4. Final Check && RUN
(2). Check RUN4 (apply new water table in blue and water loads, both in 6 increments)
(3). Check soil parameters under RUN1 (they will be carried forward, unless reassigned!!)
(4). Run versat-s2d with 4 RUNs
(a) Enter PW and Connect Now
(b). Step 2 Select file “USF_4_FINAL”
(5). results from static analysis ..

## Slide 14
5. Setup the dynamic analysis:

## Slide 15
5. Setup the dynamic analysis:
(1) Download VERSAT-2D
(2). Start VERSAT-2D Processor by “Accept” terms:
(3). under SETTING, load “USF_model.log” & under File, load data “USF_4_FINAL.sta”
(4). under SETTING : Dynamic on; click “YES”
(5). under DEFINE : General parameters, click “nonlinear effective stress...”, & new title
(6). under DEFINE : Setup dynamic analysis: (a) enter “2704” under NPRE; and (b) enter numbers for node/elem time histories (TH). – leave blank if TH not wanted. “APPLY”
(7). Under DEFINE: Input material parameters:
(a). update Kg, Kb with values listed on Table 4 (Slide No. 12),
(b). input PWP parameters in [2] hydraulic fill (using values for No. 2a in Table 4)
(c). APPLY ALL, reload this window and check!

## Slide 16
5. Setup the dynamic analysis:
(7). (b). If Wu(2001) PWP is used, then use the values in Table 3 below:
(8). Get ready to run (create a new folder “Dynamic” for dynamic analysis):
(a). under File, SAVE model data as “USF_Seed.DYN” – input master file to run in (9).
(b). copy “USF_4_FINAL.pr4” to “USF_4_FINAL.PRX” – copy results from static run
(c). manually prepare (using notepad) “USF_4_FINAL.ACX” using NOTES:
(this is already done for you !!)
(9). Run versat-d2d

## Slide 17
February 2017 Analysis Model
- 2835 Nodes and 2704 Elements Note: 678 nodes and 625 elements used in 2001 model in Wu (2001)
- subjected to 1971 San Fernando EQ Pacoima Record (PGA 0.6g) (Wu 2001)
Note: Feb. 2017 Computed displacements at Node points:
N1150 (0.77 m,-0.52 m); N1962(2.72m, -0.40m) with Seed’s PWP Model;
N1150 (0.42 m,-0.44 m); N1962(2.54m, -0.50m) using Wu(2001) PWP Model:

## Slide 18
February 2017 Analysis Results:
- Factor of Safety Against Liquefaction using Seed’s PWP model

## Slide 19
February 2017 Analysis Results:
Horizontal (X) and Vert (Y) ground displacements (m)

## Slide 20
February 2017 Analysis Results:
Computed Deformed Ground (RED) on original ground (black) with Seed’s PWP model